## Slide 1
ScalaCL and Chisel
Valdis Ādamsons

## Slide 2: OpenCL
Not to be confused with OpenGL
CLC code (i.e. the kernels) runs on the device
The kernels are called by using a C/C++ API
Supported devices:
  Most graphics cards
  Intel Phi cards
  CPUs using vector instructions
  FPGAs
  Other devices, like Adapteva Empathy processor
  etc.

## Slide 3: OpenCL computation model
The job is split into many tasks
Processing elements(PEs) execute these tasks
Each processing element(PE) does the same instructions, but on different data(task)
Not everything translates well to OpenCL 
Wavefront (aka. Warp)
Compute unit
PE “Core”
PE “Core”
Compute unit
PE “Core”
PE “Core”
…
PE “Core”
PE “Core”
PE “Core”
PE “Core”
…
…
…
Task
Task
Task
Task
…
Task
Task
Task
Task
…
…

## Slide 4: ScalaCL syntax
Test.scala
import scalacl._
import scala.math._
object Test {
def main(args: Array[String]): Unit = {
implicit val context = Context.best
val rng = (100 until 100000).cl
val sum = rng.map(_ * 2)
.zipWithIndex
.map(p => p._1 / (p._2 + 1))
.sum
println("sum = " + sum)
}
}
Exercise: spot the OpenCL here!

## Slide 5: ScalaCL syntax
Test.scala
import scalacl._
import scala.math._
object Test {
def main(args: Array[String]): Unit = {
implicit val context = Context.best
val rng = (100 until 100000).cl
val sum = rng.map(_ * 2)
.zipWithIndex
.map(p => p._1 / (p._2 + 1))
.sum
println("sum = " + sum)
}
}
Here it is!

## Slide 6: Vs Rootbeer
ArraySum.java
package rootbeer.examples.arraysum;
import java.util.List;
import java.util.ArrayList;
import org.trifort.rootbeer.runtime.Kernel;
public class ArraySum implements Kernel {
private int[] source;
private int[] ret;
private int index;
public ArraySum (int[] src, int[] dst, int i){
source = src; ret = dst; index = i;
}
public void gpuMethod(){
int sum = 0;
for(int i = 0; i < source.length; ++i){
sum += source[i];
}
ret[index] = sum;
}
}
ArraySumApp.java
package rootbeer.examples.arraysum;
import java.util.List;
import java.util.ArrayList;
import org.trifort.rootbeer.runtime.Kernel;
import org.trifort.rootbeer.runtime.Rootbeer;
import org.trifort.rootbeer.runtime.Context;
public class ArraySumApp {
public int[] sumArrays(List<int[]> arrays){
List<Kernel> jobs = new ArrayList<Kernel>();
int[] ret = new int[arrays.size()];
for(int i = 0; i < arrays.size(); ++i){
jobs.add(new ArraySum(arrays.get(i), ret, i));
}
Rootbeer rootbeer = new Rootbeer();
Context context = rootbeer.createDefaultContext();
context.init(1024*1024*4);
rootbeer.run(jobs, context);
return ret;
}
public static void main(String[] args){
ArraySumApp app = new ArraySumApp();
List<int[]> arrays = new ArrayList<int[]>();
for(int i = 0; i < 1024; ++i){
int[] array = new int[512];
for(int j = 0; j < array.length; ++j){
array[j] = j;
}
arrays.add(array);
}
int[] sums = app.sumArrays(arrays);
for(int i = 0; i < sums.length; ++i){
System.out.println("sum for arrays["+i+"]: "+sums[i]);
}
}
}
…instead of
“(0 until 512).cl.sum”

## Slide 7: ScalaCL status
Free and open source
6 lines to enable in a SBT project
Some operations might still be running on the CPU! The compiler can warn you.
Two different versions
https://code.google.com/p/scalacl/
  A Scala compiler plugin
  Functional, not production ready
https://github.com/ochafik/ScalaCL
  Implemented using Scala macros
  Work-in-progress, not yet functional

## Slide 8: Chisel
Free and open source
2 lines to enable in a SBT project
Uses Scala to “reinvent” Verilog
  Number of wires for results are inferred
  Functional constructions can create parameterized circuits
  Implicit clock available by default
  and much more
Plenty of examples available
https://chisel.eecs.berkeley.edu/

## Slide 9: A simple example
GCD.scala
import Chisel._
class GCD extends Module {
val io = new Bundle {
val a = UInt(INPUT, 16)
val b = UInt(INPUT, 16)
val e = Bool(INPUT)
val z = UInt(OUTPUT, 16)
val v = Bool(OUTPUT)
}
val x = Reg(UInt())
val y = Reg(UInt())
when (x > y) { x := x - y }
unless (x > y) { y := y - x }
when (io.e) { x := io.a; y := io.b }
io.z := x
io.v := y === UInt(0)
}

## Slide 10: More complex logic
Max.scala (fragment)
class MaxN(n: Int, w: Int) extends Module{
private def Max2(x: UInt, y: UInt) = Mux(x > y, x, y)
val io = new Bundle {
val in = Vec.fill(n){ UInt(INPUT, w) }
val out = UInt(OUTPUT, w)
}
io.out := io.in.reduceLeft(Max2)
}
…also there is an example for a simple processor – 3 registers and 2 operations. (Risc.scala)

## Slide 11: From Chisel to working FPGA
Chisel
Scala code
C simulation code
Verilog
code
Constraints
FPGA manufacturer's
tools
Device bitcode
Device
programmer
FPGA
“What pin is what?”

## Slide 12: ASICs
Application Specific Integrated Circuit – Your own custom microchips
The same Verilog code
Prices have gone down
  Shuttle services – get a piece of the wafer
  Specialized companies offer full service
  No longer a matter of millions of $, but thousands of $

## Slide 13
Thanks for your attention.
Presentation available on
https://github.com/valdisxp1/scalaCL-chisel-presentation
Any other questions?